## Slide 1
Proposal and Outline of Submarine multi beam survey line
Zecheng Zuo
Class 15 2022213434

## Slide 2
1
Introduction
2
Outline
3
Work Planned
4
Conclusion
CONTENTS

## Slide 3
Introduction
1.Introduction-Project Goal
The goal is to develop an optimized design of survey lines that improves mapping efficiency and accuracy.
The objectives include:
To describe the relationship between width, depth, and overlap rates of adjacent survey lines using planar geometric analysis.
To construct models that account for varying depths and terrain slopes in rectangular marine areas.
To optimize survey line layouts based on single-beam depth data to fully cover the target area while minimizing total survey length and avoiding excessive overlap.
Outline
Work Planned
Conclusion

## Slide 4
Introduction
1.Introduction- Single beam depth
Single beam depth measurement is a technique that uses the propagation characteristics of sound waves in water to measure the depth of water. Sound waves propagate in a uniform medium at a uniform speed in a straight line, producing reflections at different interfaces.
Outline
Work Planned
Conclusion

## Slide 5
Introduction
1.Introduction- multi beam depth
The multi beam system is developed based on single beam system. The system can emit dozens or even hundreds of beams in a plane perpendicular to the sea level, and then receive sound waves returning through receiving signals.
Outline
Work Planned
Conclusion

## Slide 6
Introduction
1.Introduction-My Work Phase 1
Outline
Work Planned
Conclusion
Firstly, I establish a one-dimensional mathematical model for the coverage width of multi beam depth measurement and the overlap rate between adjacent bands.

## Slide 7
Introduction
1.Introduction-My Work Phase 2
Outline
Work Planned
Conclusion
After Phase 1, I would consider a rectangular test area, where the angle between the direction of the survey line and the normal direction of the seabed slope projected on the horizontal plane is 𝛽. Then I establish a math model for the coverage width of multi beam system.

## Slide 8
Introduction
1.Introduction-My Work Phase 3
Outline
Work Planned
Conclusion
I have collected sounding data from a single beam survey in a certain sea area several years ago and I use this set of data to provide assistance for the measurement of multi beam survey ships.

## Slide 9
Introduction
1.Introduction-My Work Phase 3
Outline
Work Planned
Conclusion
For the Phase 3, I use a fitting algorithm to obtain the contour line fitting function as
However, based on the analysis of the contour lines, we found that there are still some areas of missed measurements on the seabed saddle surface. In order to reduce these missed measurement areas, we further optimized the selection of measurement lines at the overlap rate.

## Slide 10
2. Outline
Introduction
Outline
Work Planned
Conclusion
Part 1(abstract):
Multi beam bathymetric systems are widely used in precision seabed topographic surveys. This article aims to use geometric modeling and optimization algorithms to integrate key issues such as actual terrain, coverage width, overlap rate, and missed measurement rate in multi beam bathymetry technology. By integrating multiple objectives, the design of survey line groups is optimized to improve the efficiency and accuracy of surveying tasks.

## Slide 11
2. Outline
Introduction
Outline
Work Planned
Conclusion
Part 2(Model assumptions):
I require an overlap rate of no less than 10% between adjacent bands. This is to ensure the continuity and integrity of data to meet the basic requirements of sounding technology.
I assume that the survey line can freely turn in the sea area to meet the needs of seabed terrain exploration in different regions. This allows us to plan survey line paths more flexibly to ensure complete coverage of the entire test area.

## Slide 12
2. Outline
Introduction
Outline
Work Planned
Conclusion
Part 3(Model establishment and solution):
I have mentioned in the previous slides.

## Slide 13
2. Outline
Introduction
Outline
Work Planned
Conclusion
Part 4(Evaluation, improvement, and promotion of models):
Advantages: When establishing the model, we focus on the basic principles and geometric relationships of seabed sounding technology, omitting complex external factors, thus greatly simplifying the problem and obtaining more accurate results.
Disadvantages: Greedy algorithms and iterative methods may require a large amount of computation, especially applied in large-scale sea areas. This may result in longer computation time, especially when considering multiple parameters.

## Slide 14
3. Work Planned
Introduction
Outline
Work Planned
Conclusion
My project is planned over a 5-week period, segmented into phases:
Phase 1: Literature review and essay reading. 1 week
Phase 2: Model development for the problems and initial testing. 1 week
Phase 3: Optimization algorithm application and model refinement. 1 week
Phase 4: Final testing, analysis of results, and paper writing. 2 weeks

## Slide 15
4. Conclusion
2
3
Introduction
Outline
Work Planned
Conclusion
In conclusion, my research proposal sets a comprehensive plan to enhance the efficiency and accuracy of underwater mapping through the optimization of multibeam echo sounding survey line planning. By integrating geometric modeling and optimization algorithms, my project aims to address the limitations of current seabed mapping practices, thereby improving the collection and analysis of bathymetric data. Through the successful of this project, I expect to set new standards for MBES survey line design, ultimately leading to more precise and efficient underwater mapping techniques.

## Slide 16
CONTENTS
Thanks for your listening!